## Slide 1
GUJARAT WIRELESS PSI EXAMINATION
સંચાર ઈજનેરી
Communication Engineering — સંપૂર્ણ Revision Deck
18 વિષયો • Formula Sheet • Memory Tricks • Last-Minute Revision
GPSC | GSSSB | PSI | Wireless PSI | Class-2 & Class-3

## Slide 2
અનુક્રમણિકા
Index
1
Introduction to Communication Systems
2
Modulation — AM, FM, PM
3
AM Receiver & FM Receiver
4
Antenna & Wave Propagation
5
SSB Techniques & SSB Receiver
6
Communication Receiver
7
Line Coding Schemes
8
Pulse Modulation & Digital Modulation
9
Source Coding & Multiplexing
10
Data Communication
11
Error Detection Techniques
12
Speech Digitization & Coding
13
Switching — Space & Time Division
14
Traffic Engineering
15
Telephone Networks
16
📐 Complete Formula Sheet
17
🧠 Quick Revision & Memory Tricks
18
📰 Current Affairs
સંચાર ઈજનેરી | Wireless PSI Revision
1

## Slide 3
1
Introduction to Communication Systems
સંચાર પ્રણાલીનો પરિચય
સંચાર (Communication) એટલે Source થી Destination સુધી માહિતી (Voice, Data, Image, Video) નું પ્રસારણ.
Information
Source
Transducer
Transmitter
Channel
(Noise)
Receiver
Transducer
Destination
1
3 મૂળભૂત ઘટકો
Transmitter (પ્રેષક) — Signal મોકલે
Channel (માધ્યમ) — Signal Travel કરે
Receiver (પ્રાપ્તકર્તા) — Signal મેળવે
!
Modulation શા માટે?
Antenna Size ઘટાડવા
Multiplexing શક્ય બનાવવા
Noise ઘટાડવા & Range વધારવા
આધાર | પ્રકારો
દિશા | Simplex (એક દિશા) / Half Duplex (વારાફરતી બંને) / Full Duplex (એકસાથે બંને)
Signal | Analog / Digital
માધ્યમ | Wired (Guided) / Wireless (Unguided)
સંચાર ઈજનેરી | Wireless PSI Revision
2

## Slide 4
1
Analog vs Digital & Key Terms
મૂળભૂત પરિભાષા
બાબત | Analog | Digital
Signal | Continuous | Discrete (0,1)
Noise Immunity | ઓછી | વધુ (Regeneration)
Bandwidth | ઓછી | વધુ
Security | ઓછી | વધુ (Encryption)
★
Key Terms — વ્યાખ્યાઓ
Bandwidth: Highest − Lowest Frequency નો તફાવત
Noise: અનિચ્છનીય Signal
Attenuation: Signal Strength ઘટવી
Modulation: Message ને Carrier પર આરોપિત કરવું
SNR: Signal Power / Noise Power
📌 Modulation ના 4 મુખ્ય કારણો: Antenna Size ↓, Multiplexing ✓, Noise ↓, Range ↑
🧠
Communication System — યાદ રાખવાની Chain
Source + Transmitter + Channel + Receiver + Destination
5 ઘટકોનો ક્રમ Exam માં પૂછાય છે — ક્રમ ધ્યાનમાં રાખવો
સંચાર ઈજનેરી | Wireless PSI Revision
3

## Slide 5
2
Modulation — AM, FM, PM
Carrier Wave અને Modulation ના પ્રકારો
Carrier: c(t) = Ac sin(2πfct + φ)
Amplitude (Ac), Frequency (fc), Phase (φ) — આ 3 માંથી ગમે તે 1 બદલવાથી 3 પ્રકારના Modulation બને છે.
Parameter બદલાય | Modulation | વર્ણન
Amplitude | AM | Amplitude Modulation — સૌથી સરળ, ઓછો BW
Frequency | FM | Frequency Modulation — Noise Immunity ઉત્તમ
Phase | PM | Phase Modulation — Digital/Satellite Comm માટે
🧠
Bandwidth ક્રમ યાદ રાખો
AM < FM / PM — AM માં ઓછામાં ઓછો Bandwidth વપરાય છે
સંચાર ઈજનેરી | Wireless PSI Revision
4

## Slide 6
2
AM (Amplitude Modulation)
વ્યાખ્યા, Formula અને ઉપયોગ
Σ
મુખ્ય Formulas & લક્ષણો
Modulation Index: ma = Am / Ac (0 થી 1, ma>1 → Over Modulation)
Bandwidth: BW = 2fm
3 Components: Carrier(fc) + USB(fc+fm) + LSB(fc−fm)
માહિતી ફક્ત Side Bands માં — Carrier Power વેડફાય
✓
પ્રકારો & ઉપયોગ
પ્રકારો: DSB-FC (સામાન્ય), DSB-SC, SSB, VSB
AM Radio: 535 – 1605 kHz
Aircraft Communication
AM Frequency Spectrum
LSB
(fc−fm)
Carrier
(fc)
USB
(fc+fm)
📌 Total Power: Pt = Pc(1 + ma²/2) — Power Formula Exam માં Direct પુછાય છે.
સંચાર ઈજનેરી | Wireless PSI Revision
5

## Slide 7
2
FM (Frequency Modulation)
વ્યાખ્યા, Carson's Rule અને ફાયદો
Σ
મુખ્ય Formulas
Frequency Deviation: Δf = kf × Am
Modulation Index: β = Δf / fm
Carson's Rule: BW = 2(Δf + fm) = 2fm(β+1)
NBFM: β ≤ 0.5 | WBFM: β > 1
✓
ફાયદો & ઉપયોગ
Noise Immunity ઉત્તમ — Limiter વાપરી Amplitude Noise Remove કરાય
Capture Effect
FM Radio: 88–108 MHz, TV Sound, Mobile
📌 FM ની Noise Immunity વધુ હોવાનું કારણ = Limiter Circuit, જે Amplitude Variations (Noise) દૂર કરે છે.
3
PM (Phase Modulation) — સંક્ષિપ્તમાં
FM = PM of Integral of message | PM = FM of Derivative of message
ઉપયોગ: PSK, Digital/Satellite Communication
સંચાર ઈજનેરી | Wireless PSI Revision
6

## Slide 8
2
AM vs FM vs PM — સંપૂર્ણ Comparison
Quick Revision Table
લક્ષણ | AM | FM | PM
બદલાતું Parameter | Amplitude | Frequency | Phase
Bandwidth | ઓછી (2fm) | વધુ (Carson's Rule) | વધુ
Noise Immunity | ઓછી | વધુ સારી | વધુ સારી
Complexity | સરળ | જટિલ | જટિલ
Standard Band | 535–1605 kHz | 88–108 MHz | —
🧠
Analog ↔ Digital Correspondence — યાદ રાખો
AM ↔ ASK | FM ↔ FSK | PM ↔ PSK
સંચાર ઈજનેરી | Wireless PSI Revision
7

## Slide 9
3
AM Receiver & FM Receiver
Superheterodyne Receiver — Block Diagram
4
Receiver ના 4 Performance Parameters
Sensitivity • Selectivity • Fidelity • Image Frequency Rejection
Superheterodyne Receiver — Block Diagram
Antenna
RF
Amplifier
Mixer
IF
Amplifier
Detector
AF
Amplifier
Speaker
Local Oscillator (LO)
📌 AM Standard IF = 455 kHz | FM Standard IF = 10.7 MHz — Exam માં direct પુછાય તેવા values
સંચાર ઈજનેરી | Wireless PSI Revision
8

## Slide 10
3
Receiver Blocks — કાર્ય
દરેક Block નું કાર્ય સમજો
Block | કાર્ય
RF Amplifier | નબળા Signal ને Amplify + Preliminary Selectivity
Mixer + LO | RF ને IF માં Convert (Heterodyning)
IF Amplifier | Fixed Frequency પર મુખ્ય Gain + Selectivity
Detector | Original Signal પાછો મેળવે
AGC | Output Volume Constant રાખે
⚠
Image Frequency ⭐ — Trade-off યાદ રાખો
f_image = fRF + 2·fIF
ઊંચી IF → Image Rejection સારું, પણ Selectivity ઘટે
સંચાર ઈજનેરી | Wireless PSI Revision
9

## Slide 11
3
AM vs FM Receiver — Comparison
બાબત | AM Receiver | FM Receiver
IF | 455 kHz | 10.7 MHz
Bandwidth | સાંકડી | પહોળી
Detector | Envelope Detector | Discriminator / Ratio Detector
વધારાનું Block | AGC | Limiter + De-emphasis (75 μs)
📌 FM માં Limiter Amplitude Noise Remove કરે → Noise Immunity ઉત્તમ બને છે.
સંચાર ઈજનેરી | Wireless PSI Revision
10

## Slide 12
4
Antenna & Wave Propagation
Antenna ના Parameters અને પ્રકારો
Antenna = Transducer (Electrical ↔ EM Wave), Reciprocal Device
P
Antenna Parameters
Radiation Pattern, Gain (G), Directivity (D)
Efficiency: η = G/D
Beamwidth, Impedance, Polarization
T
Antenna પ્રકારો
Half-wave Dipole (λ/2)
Quarter-wave Monopole (λ/4)
Yagi-Uda (Directional)
Parabolic Dish (High Gain), Horn (Microwave)
સંચાર ઈજનેરી | Wireless PSI Revision
11

## Slide 13
4
Wave Propagation ના 3 પ્રકાર
પ્રકાર | Frequency | માધ્યમ | Range | ઉપયોગ
Ground Wave | LF/MF (30kHz–3MHz) | Earth Surface Follow | મર્યાદિત | AM Local Broadcasting
Sky Wave | HF (3–30MHz) | Ionosphere Reflection | ખૂબ લાંબુ | Short Wave Radio
Space Wave | VHF+ (>30MHz) | Line of Sight (LOS) | Antenna Height આધારિત | TV, FM, Satellite, Mobile
L
Ionosphere Layers
D, E, F1, F2 (F2 સૌથી અગત્યનું — રાત્રે પણ હાજર)
📌 D-Layer રાત્રે અદ્રશ્ય → રાત્રે AM Long Distance Reception સારું
સંચાર ઈજનેરી | Wireless PSI Revision
12

## Slide 14
4
Propagation — Formulas
Last-Minute Formula Revision
Σ
Critical Frequency & MUF
fc = 9√Nmax (Nmax = Maximum Electron Density)
MUF = fc × sec θ (θ = Angle of Incidence)
Σ
LOS (Line of Sight) Distance
d(km) = 4.12 (√ht + √hr)
Antenna Height વધુ → Range વધુ
📌 MUF > Critical Frequency કારણ કે Angle of Incidence (secθ) નો ગુણક લાગે છે.
સંચાર ઈજનેરી | Wireless PSI Revision
13

## Slide 15
5
SSB Techniques
Single Side Band Modulation
SSB = DSB-SC + એક Side Band Filter Out (Carrier + એક Side Band Suppress)
✓
ફાયદા
BW = fm (અડધું)
Power Saving ≈ 83%
Better SNR, ઓછો Fading
3
Generation Methods
1. Filter Method — Balanced Modulator + Sharp BPF
2. Phase Shift Method — 90° Phase Shift + 2 Balanced Modulator
3. Third Method (Weaver's) — Filter+Phasing Combination
✓
ઉપયોગ
HF Communication, Amateur Radio, Marine, FDM Telephone
સંચાર ઈજનેરી | Wireless PSI Revision
14

## Slide 16
5
SSB Receiver
!
Detection Principle
Detection = Product Detector (Envelope Detector નહીં) + BFO (Beat Frequency Oscillator) જરૂરી
📌 BFO Frequency માં Error → "Donald Duck" Audio Distortion થાય છે.
લક્ષણ | AM Receiver | SSB Receiver
Detector | Envelope | Product Detector
Local Carrier | જરૂરી નથી | જરૂરી (BFO)
IF Bandwidth | પહોળી | સાંકડી (~3kHz)
સંચાર ઈજનેરી | Wireless PSI Revision
15

## Slide 17
6
Communication Receiver
Broadcast Receiver કરતાં Advanced
Broadcast Receiver કરતાં વધુ Sensitivity, Selectivity, Stability — HF / Amateur / Military / Marine માટે વપરાય છે.
2
Double Conversion Superheterodyne
1st IF (ઊંચી — Image Rejection માટે) + 2nd IF (નીચી — Selectivity માટે, Crystal Filter)
Feature | કાર્ય
S-Meter | Signal Strength દર્શાવે
BFO | SSB / CW Detection
Squelch | Signal ન હોય ત્યારે Speaker Mute
Noise Limiter (ANL) | Impulse Noise Remove
Frequency Synthesizer (PLL) | Crystal Reference સાથે Stable Frequency
સંચાર ઈજનેરી | Wireless PSI Revision
16

## Slide 18
7
Line Coding Schemes
Binary Data → Electrical Signal
વ્યાખ્યા: Binary Data ને Transmission માટે Electrical Signal માં Convert કરવું
5
સારી Scheme ના લક્ષણો
No DC Component • Self-Synchronization • Error Detection • Noise Immunity • Bandwidth Efficiency
Scheme | વર્ણન | DC | Sync | વપરાશ
Unipolar NRZ | '1'=+V, '0'=0V | હાજર | Poor | જૂની Systems
Polar NRZ | '1'=+V, '0'=−V | ઓછો | Poor | —
Manchester | Mid-bit Transition | None | Excellent | Ethernet
Diff. Manchester | Bit-start Transition | None | Excellent | Token Ring
AMI (Bipolar) | '1' Alternately +V/−V | None | Moderate | Telephone Lines
HDB3 | AMI + Zero Substitution | None | Good | PCM (E1 — India/Europe)
📌 B8ZS (USA) vs HDB3 (Europe/India) — બંને AMI ની Long-Zero Sync Problem Solve કરે
સંચાર ઈજનેરી | Wireless PSI Revision
17

## Slide 19
8
Pulse Modulation & Digital Modulation
Sampling Theorem
Σ
Sampling Theorem (Nyquist)
fs ≥ 2fm — fs=2fm ને Nyquist Rate કહેવાય; fs<2fm → Aliasing
📌 Voice (fm=4kHz) → Standard Sampling Rate = 8 kHz
Analog Pulse Modulation
પ્રકાર | બદલાતું Parameter | Noise Immunity
PAM | Amplitude | ઓછી
PWM / PDM | Width | સારી
PPM | Position | સૌથી સારી
🧠
PAM < PWM < PPM — Noise Immunity વધતા ક્રમમાં
સંચાર ઈજનેરી | Wireless PSI Revision
18

## Slide 20
8
PCM & Digital Modulation
ASK, FSK, PSK
P
PCM — 3 પગલાં
Sampling → Quantization → Encoding
Quantization Levels: L = 2ⁿ
SQNR = 6.02n + 1.76 dB (દરેક Bit → 6dB સુધારો)
Bit Rate = fs × n → Telephone: 8000×8 = 64 kbps
Companding: μ-law (USA/Japan), A-law (Europe/India)
પ્રકાર | બદલાતું | BW
ASK (OOK) | Amplitude | 2Rb
FSK | Frequency | 2(Δf+Rb)
PSK | Phase | Coherent Det.
Noise Immunity: ASK સૌથી ઓછી → FSK મધ્યમ → PSK સૌથી વધુ
📌 QPSK = 2 bits/symbol → BPSK કરતાં બમણી Bandwidth Efficiency
🧠
Analog ↔ Digital Correspondence
AM ↔ ASK | FM ↔ FSK | PM ↔ PSK
સંચાર ઈજનેરી | Wireless PSI Revision
19

## Slide 21
9
Source Coding
Entropy & Coding Efficiency
Σ
Entropy & Coding Efficiency
H = Σ pi log₂(1/pi) bits/symbol (Theoretical Minimum Bits)
η = (H/Lavg) × 100% (Lavg = Average Code Length)
Technique | સિદ્ધાંત | વપરાશ
Shannon-Fano | Top-Down Divide (Probability Sort) | —
Huffman | Bottom-Up Combine — સૌથી Optimal | ZIP, JPEG, MP3
RLE | પુનરાવર્તિત Symbol → Count | Fax
📌 Huffman Coding = સૌથી Optimal Lossless Compression Technique
સંચાર ઈજનેરી | Wireless PSI Revision
20

## Slide 22
9
Multiplexing (MUX / DEMUX)
પ્રકાર | આધાર | Guard | વપરાશ
FDM | Frequency | Guard Band | Radio, Cable TV
TDM | Time | Guard Time | Digital Telephone
WDM | Wavelength (Light) | — | Optical Fiber
CDM | Unique Code | — | CDMA Mobile, GPS
🧠
યાદ રાખો
FDM = Analog માટે યોગ્ય | TDM = Digital માટે યોગ્ય
સંચાર ઈજનેરી | Wireless PSI Revision
21

## Slide 23
10
Data Communication
Basics, Bit Rate, Codes
5
5 ઘટકો
Message • Sender • Receiver • Medium • Protocol
Σ
Bit Rate vs Baud Rate
Bit Rate = Baud Rate × log₂(L) (L = Signal Levels)
C
Codes
ASCII (7-bit, 128 char) • EBCDIC (8-bit, IBM) • Unicode (16-bit+)
Transmission Media (Bandwidth ક્રમમાં)
Twisted
Pair
Coaxial
Optical
Fiber
(Bandwidth વધતા ક્રમમાં — ડાબેથી જમણે)
📌 Transmission Impairments: Attenuation (dB = 10log₁₀(P1/P2)), Distortion, Noise
સંચાર ઈજનેરી | Wireless PSI Revision
22

## Slide 24
10
Transmission Modes
પ્રકાર | વર્ણન
Parallel | એકસાથે Multiple Bits, ટૂંકા અંતર, ઝડપી
Serial | એક પછી એક Bit, લાંબા અંતર
Asynchronous | Start/Stop Bit સાથે Character-wise
Synchronous | Clock-based Block Transfer, Overhead ઓછો
🧠
Transmission Media — યાદ રાખો
Twisted Pair < Coaxial < Optical Fiber (Bandwidth ક્રમમાં વધતું)
સંચાર ઈજનેરી | Wireless PSI Revision
23

## Slide 25
10
OSI Model (7 Layers) ⭐
Open Systems Interconnection
7
Physical
Please
6
Data Link
Do
5
Network
Not
4
Transport
Throw
3
Session
Sausage
2
Presentation
Pizza
1
Application
Away
સંચાર ઈજનેરી | Wireless PSI Revision
24

## Slide 26
11
Error Detection Techniques
Technique | સિદ્ધાંત | Detects
Parity Check | '1' ની સંખ્યા Even/Odd | Single-bit only
2D Parity | Row + Column Parity | Single + Correct કરી શકે
Checksum | Segments નો Sum + Complement | Burst+Random (TCP/IP)
CRC | Modulo-2 Division (Generator Polynomial) | Burst Errors — સૌથી Powerful
Hamming Code | Redundant Bits ચોક્કસ Position પર | Detect + Correct Single-bit
📌 CRC Remainder = 0 → No Error | Hamming Condition: 2^r ≥ m+r+1
સંચાર ઈજનેરી | Wireless PSI Revision
25

## Slide 27
12
Speech Digitization & Coding
Analog Speech → Digital Output
Steps: Analog Speech → Sampling → Quantization → Encoding → Digital Output
PCM Parameter | Value
Speech BW | 300–3400 Hz
Sampling Rate | 8000 Hz
Bits/Sample | 8
Bit Rate | 64 kbps
Technique | Bit Rate | વિશેષતા
DPCM | <64kbps | Difference Encode
ADPCM | 32 kbps | Adaptive Step
Delta Mod. | 1 bit/sample | Slope Overload+Granular Noise
Vocoder | ~2.4 kbps | Parameter-based (GSM)
📌 PCM = Sampling + Quantization + Encoding | Standard Telephone Bit Rate = 64 kbps
સંચાર ઈજનેરી | Wireless PSI Revision
26

## Slide 28
13
Switching — Space & Time Division
S
Electronic Space Division Switching (ESS)
દરેક Call ને અલગ Physical Path ફાળવાય — Control = SPC (Stored Program Control)
Crosspoints = n × m (Single Stage); Multi-Stage → Crosspoints ઘટે, Cost ઘટે
T
Time Division Switching (TDS)
Common Path, Time Slot Share — Digital PCM Systems માટે
TSI (Time Slot Interchange): Speech Memory (Buffer) + Control Memory (Address)
SWRR (Sequential Write, Random Read) | RWSR (Random Write, Sequential Read)
📌 T-S-T (Time-Space-Time) ⭐ — Modern Digital Exchange નું Architecture
સંચાર ઈજનેરી | Wireless PSI Revision
27

## Slide 29
13
SDS vs TDS — Comparison
Point | SDS | TDS
Path | Dedicated Physical | Shared, Time Slot
Crosspoints | વધુ (n×m) | ઓછા (Memory-based)
વપરાશ | Analog / Digital | ફક્ત Digital (PCM)
🧠
યાદ રાખો
SDS = Dedicated Path (n×m Crosspoints) | TDS = Time Slot Share (TSI) | T-S-T = Modern Exchange
સંચાર ઈજનેરી | Wireless PSI Revision
28

## Slide 30
14
Traffic Engineering
Σ
Traffic Intensity (Erlang)
A = C × T / Tperiod
1 Erlang = 1 Circuit આખો સમય Busy
1 Erlang = 36 CCS = 3600 sec
Σ
Busy Hour & Grade of Service
Busy Hour (BH): સૌથી વધુ Traffic વાળો 1-કલાક
GoS = Lost Calls / Offered Calls
Standard GoS = 0.002
System | પ્રકાર | ઉપયોગ
Erlang B | Lost Call System (Queue નહીં) | Standard Trunk Sizing
Erlang C | Queuing System | Call Centers
📌 Offered Traffic = Carried Traffic + Lost Traffic
સંચાર ઈજનેરી | Wireless PSI Revision
29

## Slide 31
15
Telephone Networks
E
Elements & Topology
Elements: Subscriber Line, Exchange, Junction, Trunk
Topology: Mesh, Star, Hierarchical (Practical)
N
Numbering & Signaling
India = Closed Numbering Plan
Signaling: CCS7 / SS7 — Modern Inter-Exchange Standard
India Hierarchy (Traditional 5-Level) ⭐
LE
Local
Exchange
TAX
Trunk Auto
Exchange
PCC
Primary
SCC
Secondary
CCC
Central
Class Center
X
Exchange પ્રકારો
Local Exchange (Direct Serve) • Tandem (2 LE વચ્ચે) • Trunk/TAX (Long Distance) • Transit
📌 Evolution: PSTN → ISDN → NGN (IP-based)
સંચાર ઈજનેરી | Wireless PSI Revision
30

## Slide 32
📐 Complete Formula Sheet
Last-Minute Revision — Part 1
ક્રમ | સૂત્ર | Formula
1 | AM Modulation Index | ma = Am/Ac
2 | AM Bandwidth | BW = 2fm
3 | AM Total Power | Pt = Pc(1 + ma²/2)
4 | FM Frequency Deviation | Δf = kf × Am
5 | FM Modulation Index | β = Δf/fm
6 | FM Bandwidth (Carson's Rule) | BW = 2(Δf+fm)
7 | Image Frequency | f_image = fRF + 2fIF
8 | Image Freq. Rejection Ratio | IFRR = √(1+Q²ρ²)
9 | Critical Frequency | fc = 9√Nmax
10 | Maximum Usable Frequency | MUF = fc × secθ
11 | LOS Distance | d(km) = 4.12(√ht+√hr)
12 | SSB Bandwidth | BW = fm
13 | Nyquist Sampling Rate | fs ≥ 2fm
સંચાર ઈજનેરી | Wireless PSI Revision
31

## Slide 33
📐 Complete Formula Sheet
Last-Minute Revision — Part 2
ક્રમ | સૂત્ર | Formula
14 | Quantization Levels | L = 2ⁿ
15 | SQNR | SQNR = 6.02n + 1.76 dB
16 | PCM Bit Rate | Bit Rate = fs × n
17 | Entropy | H = Σ pi log₂(1/pi)
18 | Coding Efficiency | η = (H/Lavg)×100%
19 | Bit Rate vs Baud Rate | Bit Rate = Baud×log₂(L)
20 | Attenuation | dB = 10log₁₀(P1/P2)
21 | Hamming Code Condition | 2^r ≥ m+r+1
22 | Traffic Intensity | A = (C×T)/Tperiod
23 | Grade of Service | GoS = Lost/Offered
24 | 1 Erlang | 1E = 36 CCS = 3600 sec
25 | Crosspoints (Single Stage) | Crosspoints = n × m
26 | Offered Traffic | Offered = Carried + Lost
સંચાર ઈજનેરી | Wireless PSI Revision
32

## Slide 34
🧠 Quick Revision & Memory Tricks
Part 1
✓
Communication System = Source+Transmitter+Channel+Receiver+Destination
✓
AM=Amplitude, FM=Frequency, PM=Phase બદલાય — BW ક્રમ: AM<FM/PM
✓
AM Radio: 535–1605 kHz | FM Radio: 88–108 MHz
✓
AM IF=455kHz, FM IF=10.7MHz
✓
FM ની Noise Immunity વધુ — Limiter Circuit ના કારણે
✓
Image Frequency = fRF+2fIF; IF ઊંચી→Rejection સારું પણ Selectivity ઘટે
✓
Ground Wave→LF/MF, Sky Wave→HF(Ionosphere), Space Wave→VHF+(LOS)
✓
SSB=Carrier+1 Side Band Suppress; Power Saving≈83%; Detection=Product Detector+BFO
✓
Manchester Encoding→Ethernet; AMI/HDB3→PCM Telephone Lines
સંચાર ઈજનેરી | Wireless PSI Revision
33

## Slide 35
🧠 Quick Revision & Memory Tricks
Part 2
✓
PAM(Amplitude)<PWM(Width)<PPM(Position) — Noise Immunity વધતા ક્રમમાં
✓
PCM=Sampling+Quantization+Encoding; Standard Telephone=64kbps
✓
Huffman Coding=સૌથી Optimal Lossless Compression
✓
FDM=Frequency(Analog), TDM=Time(Digital), WDM=Optical Fiber, CDM=CDMA
✓
OSI 7 Layers Trick: "Please Do Not Throw Sausage Pizza Away"
✓
CRC=Burst Error માટે Best; Hamming Code=Detect+Correct Single-bit
✓
SDS=Dedicated Path(n×m); TDS=Time Slot Share(TSI); T-S-T=Modern Exchange
✓
1 Erlang=1 Circuit પૂરો સમય Busy=36CCS; GoS Standard=0.002
✓
India Telephone Hierarchy: LE→TAX→PCC→SCC→CCC
✓
India=Closed Numbering Plan; Signaling=CCS7/SS7
સંચાર ઈજનેરી | Wireless PSI Revision
34

## Slide 36
📰 Chapter-Relevant Current Affairs
2025–26 | GPSC / GSSSB / PSI / Wireless PSI
1
5G in India: Oct 2022 Launch, હવે 99.9% Districts Cover — 400+ Million Subscribers, 5.08 લાખ+ BTS Towers
2
BSNL 4G/5G Rollout: ₹1.64 લાખ કરોડ Revival Package, Indigenous (TCS/C-DOT) 4G Stack, 5G 2025-26 માં અપેક્ષિત
3
NFAP 2025 (30 Dec 2025 Effective): 6425–7125 MHz Band → 5G/5G-Advanced/6G; Ka/Q/V Bands → Satellite Broadband
4
Bharat 6G Alliance: 2030 સુધીમાં 6G Technology માં Global Leadership નું લક્ષ્ય
5
Satellite Communication (Satcom): FWA & Subsea Cable Landing Station Infrastructure પર ધ્યાન (દા.ત. Jio CLS, Digha)
6
Telecommunications Act, 2023: જૂના Indian Telegraph Act, 1885 નું સ્થાન લેતો નવો કાયદો
7
Digital Infrastructure Investment: Google, Amazon, Meta ભારતમાં Data Center Sector માં મોટું Investment
📌 Exam Tip: Spectrum Policy Changes, BSNL/Jio/Airtel Updates અને Telecommunications Act, 2023 પર ખાસ ધ્યાન આપો
સંચાર ઈજનેરી | Wireless PSI Revision
35

## Slide 37
All the Best!
Wireless PSI Exam માટે શુભકામનાઓ 🎯
Formula Sheet + Memory Tricks ફરી એકવાર જુઓ — Exam ના છેલ્લા 30 મિનિટ માટે આ Deck ઉત્તમ છે.